## Slide 1
J.S. Blake: President
N. Schuyler: Vice President
INTERMODAL INSPECTION PROGRAM
Notes: The Chicago Car Interchange Bureau Intermodal Inspection Program
Notes:

## Slide 2
SAFETY
Recommended PPE:
Hard Hat
Enhanced Visibility Workwear
Safety Glasses
6” Lace-up Steel Toe Boots

## Slide 4
Left
(L)
Right
(R)

## Slide 5
Left
(L)
Right
(R)

## Slide 6
Right Side Rear
(RSR)
Top Center
(TC)
Top Rear
(TR)
Right Side Center
(RSC)
Steel
Container
Right Side Front
(RSF)
Top Front
(TF)
Stacking Posts
Intermediate Headers

## Slide 7
TOP NOSE RAIL
CORNER
POST
EXTERIOR NOSE POSTS
NOSE PANELS
TOP SIDE RAIL
BOTTOM SIDE RAIL
EXTERIOR SIDE POST
STACKING POST
SIDE PANEL
FRONT CHASSIS BOLSTER
Aluminum
Container
Notes: Parts of a Domestic container

## Slide 8
Steel boxes 40ft. and under have corner castings
Steel boxes 45ft. and over have stacking posts
Bottom rail
Top rail
Corrugated panels

## Slide 9
Lockrods
Left Rear Door
Door Post/JBar
Door Header
Hinges
Rear Door Sill
DOT Under- Ride Guard

## Slide 10
Roof sheet
Roof bows
Interior side plyliners
Scuffliner
Floor
Notes: Roof sheet, Roof bows, Interior side plyliners, Scuffliner, and Floor
Notes:

## Slide 11
Chassis
Tunnel Rail
Outriggers
Bottom Rail

## Slide 12
Floor
Crossmembers

## Slide 13
(RS) Non-Gear Leg
(LS) Gear Leg
Crankshaft
Diagonal Braces
Crossbrace
Crank Handle

## Slide 14
FRONT BOLSTER
LS MAIN RAIL
RS MAIN RAIL
CHASSIS CROSSMEMBER
CHASSIS CROSSMEMBER
CROSSMEMBER GUSSET
RS MAIN RAIL
CHASSIS CROSSMEMBER
LS MAIN RAIL
LIF TIRE
LOF TIRE
REAR BOLSTER
TWIST LOCK
LOR TIRE
Notes: Chassis nomenclature

## Slide 15
FRONT BOLSTER
GLADHANDS
RS NON-GEAR LEG
LS GEAR LEG
CROSSBRACE
PUSH PIN LOCK
Notes: Front view of chassis

## Slide 16
Three Key Words for Damage
J-2
Bent
Broken
Cut

## Slide 17
4 Steps to Taking Exceptions
Location
RSF,RSC,RSR,LSF,LSC,LSR,TF,TC,TR,F,R,INT.
Item
RAIL,PANEL,DOOR,POST,ETC.
Defect
BENT,BROKEN,CUT
Dimensions
ALL DIMENSIONS ARE TO BE SHOWN IN INCHES

## Slide 18: INSPECTION TIPS
Start and finish at the same location
View intermodal equipment from all angles
Inspect underframe (crossmembers, legs, etc.)
Inspect roof (if empty, open doors; if load, use cameras, mirrors or direct visual inspection)
Check all tires
Verify initials and number
If loaded, verify seal number
Make sure doors seal properly
Tape and caulk usually cover cuts and should be written on J-1 as a cut
Denote any defects
Notes: Tips to follow when inspecting equipment
Notes:

## Slide 19
Location: Left Side Rear (LSR)
Item: Steel Side Panel
Defect: Bent
Dimension: 36”

## Slide 20
Greater than 3” deflection in horizontal bar
> 3”
DOT UNDER–RIDE GUARD

## Slide 22
Slid Flat Tire – J2 Condition
6/32 tread depth
0/32 tread depth
Notes: Damage to tire as a result of being slid flat

## Slide 23
Tire sidewall cut/punctured, exposing belt material – J2 Condition
Notes: Tire cut/punctured through one or more plies of fabric

## Slide 24
Run Flat Tire – J2 Condition
Damage to tires and tubes as a result of being run flat, resulting in discoloration, blistering,
wrinkling, and/or casing damage being evident

## Slide 25
Separated Cap – Owner’s Responsibility
Notes: Cap peeling, No Section F. damage

## Slide 26
Weather Checking – Owner’s Responsibility

## Slide 27
Worn Out Tire – Owner’s Responsibility

## Slide 28
Channel Cracking – Owner’s Responsibility

## Slide 29
Replace Noserail (Aluminum) |  |  | $629.00
Replace Noserail (Steel) |  |  | $370.00
Section Roof (4'x8' Aluminum) |  |  | $400.00
Replace Roof (Steel) |  |  | $715.00
Replace Side Panel (Aluminum) |  |  | $336.00
Replace Side Panel (Steel) |  |  | $684.00
Replace Top Side Rail (Aluminum) |  |  | $1,811.00
Replace Top Side Rail (Steel) |  |  | $2,085.00
Replace Bottom Side Rail (Aluminum) |  |  | $1,846.00
Replace Bottom Side Rail (Steel) |  |  | $2,085.00
Replace Doors |  |  | $1,114.00
Replace Doors (Steel) |  |  | $1,175.00
Replace Bias Tire |  |  | $165.00
Replace Radial Tire |  |  | $225.00
Replace Exterior Side Post |  |  | $175.00
Replace DOT Under-Ride Guard |  |  | $495.00
Replace Chassis Bolster |  |  | $1,500.00
Replace Dolly Legs |  |  | $953.00
Estimate of Repairs